## Slide 1: EasyCare
The comprehensive solution for the safest See&Treat hysteroscopies

## Slide 2: EASYcare OVERVIEW

## Slide 3: What’s in the set ?
The EasyCare set includes the following products:
  1 HD hysteroscope 2,9mm, 30°
  1 inner operating sheath 4,9mm
  1 outer operating sheath 5,5mm
  1 graduated diagnostic sheath 4mm
  4 instruments 7Fr.
  1 light cable with Storz connectors
Optional:
  a complete sterilization basket
  a 5Fr. bipolar electrode with tip
  a 5Fr. bipolar electrode button
Notes: Bien spécifier que la chemise opératoire est en 2 morceaux (3 avec l’hystéro) et que le câble de lumière n'est pas illustré

## Slide 4: A 7Fr. Operating sheath
7Fr. Instruments are more efficient, accurate and durable.
Each instrument is graduated to ease surgical marks.
Quick-Lock
connection
Distance markings on the inner and outer sheath
7Fr. Operating channel
Rotatable stopcocks
Notes: Diamètre externe n'est que de 5,5mm mais qui propose un canal de travail de 7Fr. permettant d'utiliser des instruments de 2,34mm dont les qualités sont à rapprocher de ceux de cœlioscopie de 3mm.

## Slide 5: A HD quality vision
The next generation of 2,9mm, 30°, HD Hysteroscope
High resolution images with an even distribution of the luminous intensity
Large depth of field
Autoclavable
Durable and resistant thanks to its 3 tubes design

## Slide 6: EaSYcare AND ITS COMPETITORS
Notes: Seront présentés que les chemises qui fonctionnent avec des hystéros 2,7 ou 2,9 !

## Slide 7: STORZ
Outer Ø | Inner Ø | Operating channel | The | The
5,0mm | 4,3mm | 5Fr. |  | Working lenght of 200mm No Quick-Lock No distance markings No rotatable stopcocks
5,5mm | 4,9mm | 7Fr. |  | 
Storz proposes :
Notes: Optique 2,9mm de 30°

## Slide 8: R. Wolf
Outer Ø | Inner Ø | Operating channel | The | The
5,0mm | 4,3mm | 5Fr. |  | 2,7mm endoscope of lower quality Working lenght of 205mm No Quick-Lock No distance markings No rotatable stopcocks
5,5mm | 4,9mm | 7Fr. |  | 
R. Wolf proposes :
Notes: Optique de 12 ou 30°
Optique ancienne aussi

## Slide 9: OLYMPUS
Outer Ø | Inner Ø | Operating channel | The | The
4,5mm | - | 3Fr. | Endoscope/ Sheath Quick-Lock 3mm, 30° endoscope | Working lenght of 187mm Endoscope/ sheath captive connection Monobloc sheath No distance markings No rotatable stopcocks
5,5mm | - | 5Fr. |  | 
6,5mm | - | 7Fr. |  | 
Olympus proposes :

## Slide 10: TONTARRA
Ø externe | Inner Ø | Operating channel | The | The
5,4mm | 4,3mm | 5Fr. |  | Working lenght of 194mm No distance markings No rotatable stopcocks
Tontarra proposes :
Notes: Optique 2,9mm de 30°

## Slide 11: HOW TO MAKE A DEMO WITH EASYcare ?

## Slide 12: Indications in consulting room
Patient :
Nulliparous women and infertile couples are our core targets.
Pathology : (the See&Treat pathologies)
  IUD removal
  Targeted biopsies
  Throphoblastic retention
  Minor synechiaes removal (1 and 2 types)
  Small polyps exeresis (pedicled)
Notes: L'objectif clinique étant la prise en charge sans énergie des polypes, des cloisons et des synéchies, les retraits de corps étrangers et les biopsies ciblées.

## Slide 13: Indications in OR
Patient :
Nulliparous women and infertile couples are our core targets.
Pathology :
  IUD removal
  Targeted biopsies
  Throphoblastic retention
  Synechiaes removal(1, 2 , 2.a and 3 types as appropriate)
  Polyps exeresis (up to 2cm)
  Myomas removal (0 type)
  Uterine septum treatment (fibrous)
Notes: L'objectif clinique étant la prise en charge sans énergie des polypes, des cloisons et des synéchies, les retraits de corps étrangers et les biopsies ciblées.

## Slide 14: The adjutsments of the bipolar generators for electrodes
Model | Settings | Notes
Covidien / Valleylab Force Triad | Cutting : 40 Coagulation : 60 | To increase if required by the medical condition
Erbe Vio | Cutting : Effect 3 Coagulation : Effect 3 | Possibility to lower these values but keep Effect 3 for standard use
BOWA | Cutting : Effect 2 Coagulation : Effect 2 | 

## Slide 15: Tips & tricks
Inquire beforehand about the equipment available: bipolar generator and light source
  Provide appropriate cables/connectors.
On the demo’s day:
  Set the generator correctly (if electrodes are used in OR)
  Assist the doctor to assemble EasyCare
  Recommend a dilatation up to 5,5 (if in OR)
Notes: Parler de la possibilité de faire des essais mixant ReseCare & EasyCare

## Slide 16: exAmple

## Slide 17: Synechiaes removal by Pr. Fernandez